ATMOS INSTRUMENT DEVELOPMENT AND TESTING

     
                           Background

The current ATMOS instrument represents the outgrowth of an atmospheric measurement
program begun at the Jet Propulsion Laboratory (JPL) in 1972 using a flight model High
Speed Interferometer (HSI) designed and built by the Laboratory for use on aircraft and
balloon borne platforms.  The original instrument, designated the Mark I, covered the
wavelength region from 1.8 to 5.2 micrometers with an unapodized resolution of 0.125
wavenumbers.  This instrument, which was flown on a wide variety of aircraft and balloon
borne platforms, gathered information on the mixing ratios of atmospheric minor and trace
species from ground level to a height of 40 km.  Among these measurements were several
stratospheric "firsts," including the first spectroscopic detection of NO, the first NO/NO2
ratio, the first spectroscopic detection of HCl, the first HF/HCl ratio, and the first profile
for HF in the 20 to 40 km region of the atmosphere.

During the 1976-1977 time period, a Shuttle Definition Study was conducted both to
determine the feasibility of acquiring infrared interferometric data from the Space Shuttle
and to provide a conceptual design for an instrument capable of making the measurements. 
This study culminated with the award of a contract to Honeywell ElectroOptics Center
(HEOC) in January 1978 to design and build the ATMOS sensor.  The following paragraphs
describe the design and development of the ATMOS instrument by HEOC.

                       Instrument Overview

A block diagram of the functional elements of the ATMOS instrument is shown in Fig. 2. 
Radiation enters the instrument via a suntracker and a foreoptics subsystem, with the latter
defining the FOV and the size of the beam.  The energy rejected by the field stop is
reflected to a frame camera and is recorded as an image of the Sun with the position of the
FOV of the instrument superimposed.  The wave front passing through the field stop is
divided by the beamsplitter and modulated by the moving elements in the interferometer. 
The modulated radiation leaving the beamsplitter passes through one of the six selectable
bandpass filters and is focused on a Mercury Cadmium Telluride (HgCdTe) detector
operating at 77 K.

The signal produced at the detector is conditioned and digitized by the Signal Handling
Subsystem (SHSS).  The digitized signal is then formatted by the Data Handling Subsystem
(DHSS) into a Pulse Code Modulated (PCM) data stream.  This signal is then output to the
instrument Ground Support Equipment (GSE) or, during a flight, directly to the Shuttle
High Rate Multiplexer (HRM).  Additional engineering and housekeeping data is processed
by the Engineering Data Handling Subsystem (EDHSS) and is output as a part of the high
rate data stream as well as in a separate low rate engineering stream.  All command and
control functions for the instrument are performed by the Command and Control Interface
Subsystem (CCISS).

                     Instrument Description

For purposes of discussion, the ATMOS instrument, shown in Fig.  3, can be divided into
two sections: (1) the optical sensor, composed of all the optical subsystems and the scan
servo control unit, and (2) the electronic assemblies, including the compressor for the
detector cooler.  All the elements of the optical sensor are mounted to an aluminum
baseplate that in turn is mounted via vibration isolators to a substructure assembly.  This
assembly attaches to, but is thermally isolated from, a platform located in the payload cargo
bay of the Shuttle.  An aluminum cover, which also mounts to the baseplate, encloses all but
the suntracker and camera.  The internal pressure of the sensor is maintained at ambient
through a vent that is fitted with a desiccant filter assembly designed to provide a clean, dry
environment under all conditions.

The electronics section is mounted on a secondary support platform that is mechanically
isolated from the main support structure via vibration isolators.  The electronics are
physically separated into two units, one chassis containing the SHSS, DHSS, EDHSS, and
CCISS and the other containing the power supply subsystem.  A thermal control plate
mounts to the underside of the secondary platform and provides a nominal thermal
operating range of +5øC to +45øC under pallet conditions ranging from -150øC to +120øC.

Suntracker and Foreoptics

The optical layout for the suntracker and foreoptics, including the frame camera optics, is
shown in Fig.  4.  The two axis servo controlled suntracker tracks the Sun to an accuracy of
0.4 mr with a stability of 0.06 mr.  Sun detection and positive feedback are provided by a
silicon quadrant array with an acceptance cone angle of 20 deg.  In the tracking mode, the
sensor's FOV is centered on the solar disk; however, commands can be sent to offset the
tracker null position in 1 mr steps to avoid (or seek out) sunspot activity.  The tracker can
be prepositioned to intercept the Sun at the appropriate time for a subsequent sunset or
sunrise encounter by a commandable pointing capability that provides near hemispheric
coverage.

Energy reflected by the suntracker passes through a Zinc Selenide (ZnSe) window and
enters the foreoptics.  The cover window is Anti Reflective (AR) coated for improved
efficiency in the 2 to 16 micron region without significant loss at the camera wavelength of
0.575 microns.  The foreoptics telescope has a 7.5 cm diameter collecting aperture and
consists of two confocal F/3 off axis paraboloids with a selectable field stop located at their
common focus.  Field stops corresponding to instrument FOVs of 1, 2, and 4 mr can be
selected.  Energy passing through the stop is recollimated by the telescope secondary and
transferred to the interferometer.  Angular magnification is restricted to 2.6 because of
obliquity limitations within the interferometer.  The rejected energy is reflected to the frame
camera via an ellipsoidal mirror.  One solar image is recorded by the camera at the end of
each 100 cm scan.

Interferometer

A block diagram of the optical layout of the interferometer is also shown in Fig.  4.  The
optical system is a modified version of the classical Michelson interferometer that uses cat's
eye retroreflectors in place of plane mirrors and double passing techniques for maximum
alignment stability.  The design relaxes component alignment tolerances from a few arc
seconds to several arc minutes, thus rendering the instrument insensitive to mechanically or
thermally induced misalignments.

Energy enters the interferometer through an aperture in the common retro mirror and
impinges on the beamsplitter at an angle of incidence of 45 deg.  The beamsplitter substrate
is Potassium Bromide (KBr) with a Ge/KRS-5 coating designed for optimum efficiency over
the 2 to 16 micron region.  Radiation reflected from the beamsplitter passes through a KBr
compensator plate and goes to the cat's eye retroreflector, which consists of an F/2.7
paraboloid primary and a slightly convex secondary.  The radiation exits the cat's eye
displaced, travels through the compensator, and is reflected off a gold coated area on the
beamsplitter substrate that directs the energy to the retro mirror.  The reflected beam then
retraces its path back to the beamsplitter surface.  The radiation transmitted by the
beamsplitter follows a similar path but uses the beamsplitter substrate in transmission rather
than in reflection.  The Optical Path Difference (OPD) is varied continuously from +50 cm
to -50 cm at a retardation rate of 50 cm/s by moving both cat's eyes equal distances in
opposite directions.  This has two advantages over a single moving element system: first, it
decreases the mechanical scan rate to 6.25 cm/s, half its former value; and second, by
scanning the cat's eyes in opposite directions, it rejects common mode forces, thus providing
for a first order velocity correction.  Requirements for high spectral data quality dictate
precision control of the OPD scan to a velocity uniformity of 0.1% peak to peak.  This level
of performance is achieved through the use of a frequency stabilized HeNe laser for OPD
velocity feedback.  The reference laser used in the ATMOS interferometer is a modified
Hewlett Packard HP5501A Zeeman split actively stabilized laser providing single mode,
single frequency output at 0.6330 microns.  The laser energy passes through the
interferometer parallel to the infrared beam.

The key elements of the scan servo subsystem are shown in Fig.  5.  The velocity servo is
implemented with two control levels: (1) an outer control that uses a phase locked loop to
convert laser feedback to an error signal and provides the precise velocity control; and (2)
two inner control loops, one for each slide, that use moving coil tachometers for velocity
feedback.  The function of the inner loops is to force both slides to operate at approximately
the same velocity.  As each slide reaches the end of its travel, control is switched to position
feedback with the loop closed around Linear Variable Differential Transformer (LVDT)
position sensors; the return scan is initiated after both sliding assemblies are brought to a
halt in their hold positions.  To maximize the duty cycle, scan control is provided in both
directions with turnaround times of 150 ms at each end.

The output from the interferometer passes through one of the six selectable bandpass filters
and is focused by an AR coated ZnSe lens onto a photoconductive HgCdTe detector, where
a pupil image is formed.  The detector is a single element, 27 mils on a side; the size of the
chip was chosen on the basis of both sensitivity and linearity requirements under high signal
flux conditions.  It is AR coated to improve quantum efficiency and uses a constant bias
voltage to improve linearity.  The element is packaged in a sealed glass vacuum dewar and
cooled to 77 K using a split Stirling cycle mechanical cooler with a 1.6 watt cooling capacity.

                     Electronics Description
 
The output from the detector is transferred to the SHSS, where it is amplified, filtered, and
digitized for insertion into the DHSS.  The SHSS, shown schematically in Fig. 6, has been
designed to preserve source noise limited performance while accommodating an expected
dynamic range of 18 bits with minimum phase and amplitude distortion.  The 18bit dynamic
range, high data rate operation is obtained through the use of two 12 bit parallel data
channels offset in gain by 5, 6, or 7 bits, selectable by command.  Both outputs are included
in the PCM data stream.  During ground processing, valid data from each channel is
interleaved to reconstruct an effective 18 bit signal that preserves peak signal precision and
maintains source noise limited performance at high spectral resolution.  Sampling of the
analog interferogram in both channels is based on delayed reference laser fringe sampling
at every second (395 kHz) or third (263 kHz) laser fringe, selectable by command. 
Electronic distortion has been minimized through
proper delay of the sampling waveform as well as through use of multipole compensated
Butterworth filters for noise bandlimiting.
 
The remaining elements of the ATMOS electronics are shown in Fig.  7.  The DHSS accepts
the digitized high and low gain interferometric data to be buffered and formatted into a
Shuttle compatible Non Return to Zero Logic (NRZ L) serial 15.76 Mbit/s PCM data
stream.  The formatting section is a hard wired design with formatting accomplished by a
digital multiplexer.  The high rate data format includes the engineering and housekeeping
data and both time and optical path position references.  Also shown in the block diagram
are the main elements of the EDHSS and CCISS.  A common feature of these subsystems
is a Motorola MC6802 microprocessor that formats the system engineering and
housekeeping data as well as decoding and implementing the instrument commands received
through the Shuttle interface.  In addition to the high rate PCM data channel, the ATMOS
instrument provides a 1.28 kbit/s low rate PCM output containing engineering and
housekeeping data only.