Since the molecules of interest to the ATMOS investigation must be measured remotely
(i.e., from outside the atmosphere itself), solar spectroscopy was the obvious method for
making the measurements, using those periods during each orbit of the spacecraft when the
atmosphere is between the Sun and the instrument (i. e., at sunrise and sunset as seen from
the spacecraft).  During sunset, for example, the tangent point of the ray path to the
instrument penetrates deeper and deeper into the atmosphere until it is blocked by the
surface of the Earth (or clouds); as seen from a typical shuttle orbit, the height of the
tangent point changes at about 2 kilometers per second so that, to be able to distinguish
changes in the composition with altitude, successive measurements of the spectrum must be
made very rapidly.  By analyzing the absorptions due to a given molecule in each successive
spectrum, the variations in its concentration with altitude can be determined.

The rapidity at which the measurements must be made precludes the use of conventional
scanning spectrometers which record the spectrum wavelength by wavelength, requiring
minutes or even hours to cover relatively modest wavelength intervals.  Furthermore, such
instruments by their nature are limited to collecting radiation through very narrow entrance
apertures. Thus, only a small amount of light enters the instrument, and only a very small
fraction of that light is measured at any given time.

A technique which overcomes these limitations is based on the interference properties of
light waves, and was first used in an analytical instrument by Albert Michelson almost a
century ago.  This technique, called interferometry, does not involve dispersion of the
radiation being analyzed, and hence it can be admitted to the system through much larger
apertures than the slits required for scanning instruments.  Once inside, the radiation is split
into two beams which travel separate paths through the instrument and are then
recombined.  If the length of one path is varied with respect to the other, the various
wavelengths of light contained in the recombined beam will go in and out of phase as a
function of the wavelengths themselves and the path difference.  If the recombined beam
is then focussed on a detector and sampled at the proper intervals, a signal called an
interferogram is produced which is extremely complex but can be transformed to yield the
amount of radiation contained in the original beam as a function of wavelength.  Since
information about all wavelengths of light in the beam is contained in every sample
recorded, the technique is not subject to the second limitation of scanning spectrometers
mentioned above.

Although the concepts involved in interferometry are straightforward, the instrument itself
must work in the realm of fractions of wavelengths of the light being measured and thus
severe demands are placed on the fidelity of the optics and the precision and accuracy of
the sampling intervals.  But for the advent of high stability single-frequency lasers, ultra-fast
electronic components, and modern optical polishing techniques, the ATMOS sensor could
not have been built.  The instrument uses optical components polished flat to within a
twentieth of the shortest wavelength of the light being measured, and generates an
interferogram containing 400,000 sample points (the intervals between which are precisely
controlled using a reference laser) every second!  The corresponding rate at which the data
are transmitted to the ground is 16 million bits per second.